## Slide 1
2023 – CLAMPS & CopterSondes
Lake Village, AR:
CLAMPS2 continuous deployment
Doppler lidar: VADs, vertical stares, backscatter
MWR: TROPoe temperature and humidity retrievals, sfc met
AERI not on board
CopterSonde WxUAS IOP deployment
  Pressure, temperature, humidity
  Wind speed and direction
Schlater, MS
CopterSonde WxUAS IOP deployment
  Pressure, temperature, humidity
  Wind speed and direction
Yazoo City, MS
CopterSonde WxUAS IOP deployment
  Pressure, temperature, humidity
  Wind speed and direction
Note: CLAMPS1 did not deploy

## Slide 2
CLAMPS2 VAD
Lake Village: 33.36354N, 91.262W
2023
IOP1
IOP2
IOP3
IOP4
IOP5

## Slide 3
CLAMPS2 Stare
Lake Village: 33.36354N, 91.262W
2023
IOP1
IOP2
IOP3
IOP4
IOP5

## Slide 4
CLAMPS2 MWR TROPoe
Lake Village: 33.36354N, 91.262W
2023
IOP1
IOP2
IOP3
IOP4
IOP5

## Slide 5
2023
Coming REALLY soon to data archive!

## Slide 6
2023 NSSL lidar Truck
8-pt VADs every 5 minutes with vertical stares in between, with 30-m range gates
Deployed for all 5 IOPs near center to southeast portion of the radar config.
Started ~t0 – 4 h and ending as precip. overtakes location (or meso approached as in IOP4)
Data mostly complete (outside precip./fog/etc.) except for last ~2 h of IOP4 (user error )
Released Windsonds within 1-h of convection, as frequently as every 3-min
Data still in the queue to be QC’ed
Halo Photonics Streamline XR+ Doppler lidar
  ~ 12 km range (depending on aerosol properties), but typically 1-2 km in vertical (in cloud & precip. free conditions)
  Bandwidth +/- 38 m s-1

## Slide 7
2023 Lidar Truck … data processing ongoing
Issue: Persistent + or - w fields superimposed on reasonable measurements
Source: Likely issues with lidar leveling (mechanical, user-based, or extreme broad-side winds)
Solution: Pitch/roll corrections; different for every deployment. Work ongoing
Pitch Roll

## Slide 8
Created by OU UG Victor Alvarez
https://apps.nssl.noaa.gov/CLAMPS/data/
CLAMPS
Web Access
THREDDS
Data Access
Data Viewer
Get started using our data with tools at bliss.science/resources/code